## Slide 1
Project Beebot: Swarm Robotics Platform
EG / 2021 / 4458 - Dayananda G. G. A. I.
EG / 2021 / 4605 - Kasthuriarachchi K. A. A. D.
EG / 2021 / 4858 - Weerasiri G. M. I.

## Slide 2
System Architecture
Overhead Camera
A 1080p HD camera that localizes the robots and identifies AR markers for accurate positioning.
Central Platform Microprocessor
Utilizes a Raspberry Pi to coordinate the swarm robots and manage their task allocation.
ESP-32 Based Robots
Each robot is equipped with an ESP32 microcontroller, which communicates wirelessly with the central Raspberry Pi.
3D Web Interface
Provides interactive visualization and control of robots through a Three.js-based platform.

## Slide 3
Firmware Flow Chart

## Slide 4
Robot Design & Hardware
Core Components
ESP32 Microcontroller with Wi-Fi/Bluetooth
Motor Driver: TB6612FNG, durable and efficient
Gyroscope for heading correction
Power & Structure
2 LiPo Batteries, 800mAh at 7.4V
Dot Board chassis, lightweight and modifiable
Compact and efficient circuit layout for space optimization

## Slide 5
Proteus Design

## Slide 6
Project Progress So Far
Robot Development
Created one of two swarm robots equipped with ESP32 and sensors.
AI Marker & Image Processing
Generated AI marker and implemented image processing to identify robots from overhead camera.
3D Interface
Partially developed 3D web interface displaying the arena.
Hardware Design
Designed PCB layouts and schematic diagrams for robot electronics.

## Slide 7
Future Work and Remaining Tasks
1
Create Additional Robot
Develop the second robot for the swarm platform.
2
Set Up Server and Backend
Establish a server to host the 3D web interface for visualization and control.
3
Develop Robot Algorithms
Design and implement algorithms to enable swarm behaviors and obstacle avoidance.
4
Configure Raspberry Pi
Set up the Raspberry Pi as the central unit coordinating robot tasks.
5
Implement Communication Protocols
Manage MQTT and other protocols for reliable robot-central unit communication.

## Slide 8
Thank You
We appreciate your time and attention.
Please feel free to reach out with any questions or feedback.